## Slide 1
Signals
for Amateur Radio
Jeff - KØZR

## Slide 2: Signals
Earliest beginnings were
  Beats on a drum (cave man days)
  Puffs of smoke ( Indian days)
  Wave a flag to the left or the right
  Presence or absence of a voltage ( Morse “clicks”)
  …
Modulation – a term birthed in the earliest days of radio
  Simplest form: amplitude, frequency, or phase of a carrier is varied in accordance with the sound waves or other intelligence to be transmitted
  Carrier is the signal vehicle used to convey the information

## Slide 3: Advances in Communication
Technology rarely advances in complexity or capability without some market driving force
  Increased efficiency of data transmission
  Improved error-free transmission
  Higher volume of data passed per unit time
  Conservation of limited frequency spectrum
  SWAP: size, weight and power of hardware
  Manufacturability, affordability of hardware

## Slide 4: A Journey Through Communications
Morse Code
AM and SSB
NBFM – narrowband FM
Standard FM
Noise and its impacts
Digital Waveforms – constellation diagrams
  BPSK – binary phase shift keying
  QPSK – quadrature phase shift keying
Coding
FT8

## Slide 5: Morse Code
Series of ON/OFF tones
The “code” itself was designed to:
  Expedite letters used most frequently
  Minimize overall character length while accommodating the 26 basic latin letters
  Promote intelligibility
  Offer a level of noise/interference immunity
A “Dit” is one time unit in length
A “Dash” is three time units in length
Interelement gap is one time unit or “Dit” in length

## Slide 6: Morse Code - 2
The shorter the “dit”
  Wider channel bandwidth required
    More noise enters the channel
  Channel bandwidth places upper limit on the dit-dah rate possible
Transmitter and receiver among the simplest possible
  Receiver determines presence/absence of signal
  Distinguish sequence of dots and dashes
In 2005 a Belarus amateur transmitted 230 Morse code marks of mixed text in one minute

## Slide 7: Morse Code - 3
Using the Dit-Dash timing principles of Morse a mathematical expression for the time required to send “LARG” was quickly developed
  1 Morse word is 5 characters
  20 WPM (words per minute) equates to 100 characters in a minute
  Required bandwidth is simply 1/(time of one bit)
    This is a rudimentary approximation for comparison only

## Slide 8: Morse Code - 4
The shorter the bit the
higher the code rate
Bandwidth increases
proportionately to code rate

## Slide 9: Morse Code - 5
Using information presented, a code rate of 20 WPM requires 12.5 Hz of bandwidth
Compare this to what is needed for standard SSB
10 log10(12.5) = 10.97 dB-Hz [CW]
10 log10(2700) = 34.31 dB-Hz [SSB]
CW enjoys 23.34 dB-Hz advantage over SSB
  Actually more because of intelligibility issues
A CW signal utilizes its bandwidth much more efficiently than SSB
The Morse receiver is very complex – a human ear that can decipher Morse code

## Slide 10: AM and SSB
Amplitude Modulation (AM) was the first of the true modulations invented
  Simple hardware for transmitter
  Simple hardware for receiver
  Spectrally very inefficient
  Modulation efficiency, the power actually embodying the intelligence on the signal, is poor
  100% The highest efficiency possible is 50% for a square wave
AM requires ~ 6 kHz bandwidth while SSB ~ 2.7 kHz
ALL the power in a SSB signal goes into the sidebands to represent the intelligence
  66% of the power in AM is in the do-nothing carrier
  No wasted power in a carrier for SSB

## Slide 11: NBFM – 2m and 70 cm FM
All handhelds use narrowband FM
  Closely related to AM and SSB mathematically
NBFM is simple, offers good noise immunity, and signal is not overly wide
Carrier Modulation
Standard AM/SSB
NBFM
Modulation at 90o
Integral to any FM receiver is a limiter which
attenuates atmospheric and manmade noise
Carrier

## Slide 12: Standard FM
Frequency modulation more complex; greater bandwidth required; must be optimized
Frequency modulation index is
=
98% of total power is contained in the BW
where B is the bandwidth of the modulating signal
Known as Carson’s Rule
FM signals have carriers and optimum modulation indexes reduce the amount of power wasted there
The zeroth order Bessel function determines the amount of carrier power present

## Slide 13: Standard FM - 2
Power in a FM signal is described by a summation of Bessel functions:
Each Jn term is a Bessel function;
J0 determines the size of the carrier
Mod indices of 2.4, 5.52, etc. produce zero power in the carrier
  Best use of the transmitted power

## Slide 14: Noise
Just like death and taxes, noise is always with us in comm systems
  Noise is the nemesis of all communication systems
Standard, untainted noise is called white noise
  If passed through a filter or changed by electronic circuits, can become a different type of noise, colored noise, which has different statistical properties
The radio/channel designer must:
  Structure the channel to limit noise
  Devise modulation formats which offer improved noise immunity, even corrections for errors caused by noise
  Modulation formats which are more tolerant to nonlinearities in amplifiers or nonlinear phase found in most filters
  Some processing inherently makes noise worse
    Any operation that takes the derivative of the signal generates noise

## Slide 15: A Digression into BPSK
The simplest type of digital signal today (not counting CW) is BPSK – binary phase shift keying
A signal constellation diagram for BPSK is
-1
+1
Perfect, noise-free BPSK
-1
+1
BPSK With Noise

## Slide 16: A Digression into BPSK - 2
How can a “-1” be received:
  A “-1” is actually transmitted
  A “+1” is actually transmitted and erroneously interpreted as a “-1”
A “+1” signal incorrectly interpreted as “-1”

## Slide 17: A Digression into BPSK - 3
How can a “+1” be received:
  A “+1” is actually transmitted
  A “-1” is actually transmitted and erroneously interpreted as a “+1”
A “-1” signal incorrectly interpreted as “+1”

## Slide 18: A Digression into BPSK - 4
The probability of obtaining an error is:
  A “-1” is sent but interpreted as a “+1”
  A “+1” is sent but interpreted as a “-1”
= (Prob of error)

## Slide 19: BPSK and Noise
In all digital signaling, decision boundaries are integral to demodulating the data
-1
+1
Signal to the right is interpreted as a “1”
Signal to the left is interpreted as a “-1”
Hard decision boundary
Advanced demodulation techniques use soft decision boundaries

## Slide 20: More than BPSK
BPSK is the simplest; today much more complex formats such as 64 – QAM (quadrature amplitude modulation) or 64-PSK (phase shift keying)
000111
001100
With more complex signal constellations,
one “point” can convey much more
information
As shown, each point conveys 6-bits of information
Increased sensitivity to phase and amplitude
inaccuracies ( and noise )

## Slide 21: Increasing Channel Throughput
Using a more complex “alphabet” or signal constellation enables more rapid data transmission
Integrity of the channel becomes increasingly important with more complex constellations
  Phase linearity
  Amplitude linearity
  Noise of all types to include phase noise
  Manner in which signals are filtered
  Accuracy of frequency sources for sampling and frequency translation

## Slide 22: Nothing is Free
In the late 1940’s several researchers identified the limitations on the amount of data that can be passed through a channel
  These limitations are true today
  Generally called the Shannon Capacity Theorem
Error-free transmission can be achieved at any rate lower than the capacity predicted
No one has “beaten” the capacity theorem although modern techniques are getting closer and closer
C = bits/sec W = bandwidth Eb = energy per bit

## Slide 23: Channel Coding
Of great importance in today’s digital signaling is coding:
  Encode a signal to be more tolerant of nonideal conditions
    Grey codes, 8b10b coding, Manchester, differential, Trellis, etc., etc.
  Augment intelligence with a FEC – forward error correction code
    Adds “overhead” to the signal BUT can self-correct some bit errors as they occur
    Many, many types:
      BCH
      Reed-Solomon
      Convolutional
        Trellis
        Viterbi
      Turbo
  Codes can be layered on top of one another; adds security
    Without knowledge of the “key code”, cannot decipher it

## Slide 24: What About FT8?
Imagine two situations where you, the receiver, must determine when the letter “E” ( a dot ) is sent in Morse code
Time length = 60 seconds
Time length = 7.5 seconds
In low to marginal signal conditions, noise and other interference is present, increasing the chances an incorrect detection occurs in the 60 seconds
In FT8 due to very accurate time keeping, your receiver knows to listen to only 7.5
seconds and disregards the other 52.5. This improves the error rate and allows
signal levels to be even lower in strength
* Numbers chosen only to illustrate principles

## Slide 25: What About FT8 - 2?
FT8 works by sending signals in 15-second-blocks with 12.64 seconds of transmission time and 2.36 seconds of decode time
This allows FT8 transmission to support up to 13 characters
FT8 employs 8-FSK (frequency shift keying) format in a signal bandwidth of only 50 Hz.
  Standard FSK (RTTY) uses two tones separated by 170 Hz
FT8 also employs forward error correction (FEC) coding
  Signals are “pre-encoded” such that at the receiver they are more accurately received
  Some FECs can self-correct one or possibly two mistakes; the more the correction the more overhead embodied in the coded signal
Accurate time stamps are critical to successful FT8
  A wandering computer clock will instantly cease FT8 reception/transmission