## Slide 1: Yet Another Go Box (This is Mine)
Steve Greene, KS1G
LARG November 18, 2023

## Slide 2: “Go Kit” / “Go Box”
Go Kit: A collection of ham radio gear you can grab and go; a complete station in a transportable package
Go Box: Same stuff packaged so you can operate w/o assembly

## Slide 3: Why?
STOP! Tearing station apart for Field Day, Public Service Events, Travel
STOP! Rebuilding station after Field Day, Public Service Events, Travel
STOP! Fixing connections, settings just to get on the air
GO! Grab-and-Go!
GO! Protect my gear
GO! Inspired by Field Day, Reston Century stations, K4HCO’s Go-Box talk at August LARG meeting

## Slide 4: What Did I Want?
HF station in a box (bonus if VHF & UHF)
All modes – CW, SSB, Digital, FM
Up to 100W TX
Work with variety of antennas
Minimal setup at operating site
Protect equipment from environment during transport, storage
Hand-carry, car transport

## Slide 5: Use Gear I Already Have
FT-857 Transceiver
High-capacity battery, sort-of boxed
Familiarity with small single-board PCs
Weather-resistant hard case

## Slide 6: So, What Did I Do?
Already Had:
FT-857 in mobile mount
Separated control head, Raam Mount
DigiKey interface
HF “Apache” 3800 hard case
Separate Battery Box
Wireless keyboard, mouse for computer
Portable Display (or VNC to tablet)
Bought for this project:
LDG Z-100 Plus 100W auto-tuner
ATOPNUC Single Board x86 computer
Power Distribution

## Slide 7: Other Bits & Pieces
Coax Feed Throughs – Max Gain Systems
4 port “Rig Runner” with side input – electro-resales (Ebay)
Multi-port QC/PD USB Charger
Hole Saw, Step Drill
Nuts, bolts, coax, hook-up wire, …
Label everything!

## Slide 8: I Think it Turned Out Pretty Nice!

## Slide 9: Battery Box
High capacity 60AH LiFePO4 battery
Master Fuse/Circuit breaker
Power monitor
Fuse Block (bought for this project)
PowerPoles for Radios/high current devices
USB Ports
Charging Port
HF “Apache” 2800 hard case
Or self-contained: I can just fit a 12AH battery in the radio case

## Slide 10: Battery Boxes (I built two)

## Slide 11: About the Computer & Software
ATOPNUC Single Board x86 computer
  Runs on 12V DC!
  Wifi, Bluetooth, video on USB-C
O/S: Linux Mint
KM4ACK “73 Linux” (successor to “Build A Pi”)
  Hotspot, “headless” with remote access via VNC
  GPS support
  FL Suite: FLDigi, FLRig, etc.
  WSJT-X
  YAAC APRS, Direwolf
  WinLink (Pat Client) & VARA modems
  Logging
  …more

## Slide 12: 73 Linux (Screenshot)

## Slide 13: 73 Linux (Screenshot)

## Slide 14: What’s Next?
(More) Practice operating from home station, backyard/driveway
Work on antenna selection
Plan and do portable and local POTA ops
Do I want to do this for satellites?

## Slide 15
73s & Thanks!
de KS1G

## Slide 16: Vendors & Sources for Go-Box Components
Tuner: LDG Z100 Plus
Ebay: Power Distribution “electro-resales”; RJ45 extension (FT857 mic)
DigiRig: Computer-radio interface and FT-857 cables
Amazon:
  ATOPNUC Mini PC Ubuntu, AMD A9 9400Single Board x86 computer
  Nilight Quick Charge Socket PD Type C and QC3.0 Dual USB Charger
  DaierTek 12V Fuse Block 6 Way with LED Indicator Light 12 Volt Fuse Box ATO/ATC
  ZAXIDALER Rectangular External Communications Speaker
  NECABLES 2Pack RJ12 6P6C Male to Male Straight Wired for Both Data and Voice Use
Max Gain Systems – Coax feedthrough kit with large gaskets, washers, nuts 7518-UHF-BC-3-PRO (3” feedthrough kit)
Powerwerx: PowerPoles, panel mount sockets
Cases: Harbor Freight: “Apache” 3800 (Radio box) and 2800 (Battery boxes)