## Slide 1: Presentation to LCARES
Steve
N4RAF
7 Jan 26

## Slide 2: What is Winlink?
Winlink Global Radio Email®️...
...is a network of amateur radio and authorized government stations that provide worldwide radio email using radio pathways where the internet is not present.
…is an all-volunteer project of the Amateur Radio Safety Foundation, Inc. (ARSFI), a non-profit public benefit corporation with no beneficial owners.
Aka Winlink 2000 Network
https://www.winlink.org/

## Slide 3: What is Winlink?
Origins with sailing community in 1990s
Worldwide radio email service that uses RF
  HF
  VHF/UHF
Supports attachments, position reporting, weather and information
Used for emergency and disaster relief comms
  Some level of ‘protection’ since it isn’t voice
  Higher quality vs. voice
No internet required
  Using smart-network radio relays

## Slide 4: Winlink Was There...
Lives and property saved, damage mitigated and training, training, training: Why Winlink volunteers do what they do. Here is a sampling of events and incidents in which the system was significantly involved.
Winter 2021 Texas Freeze
Fall 2020 Nationwide Red Cross Exercise
Fall 2020 Ohio Military Reserve "Black Swan" Exercise IPAWS Demonstration
2020 California Earthquakes
2019 Citadel Rumble CA Exercise
2019 Washington State EOC-EOC Exercise
2019 Mexican wildfires,
https://winlink.org/
An article describing how radio amateurs can help fill the information “donut hole” by providing post-earthquake “did you feel it” (DYFI) reports via Winlink HF radio email appeared on February 22 in the American Geophysical Union (AGU) magazine Eos.

## Slide 5: Users
Amateur Radio Emergency Service® (ARES®)
Radio Amateur Civil Emergency Services (RACES)
CISA - SHAred RESources (SHARES) High Frequency (HF) Radio Program
American Red Cross
Hospitals
US Government – Dept of Homeland Security – FEMA
MARS
County Governments
AT&T
FedEx
Us Hams

## Slide 6: Terms and Definitions
Client stations (radio operators) connect by RF to an RMS.
RMS: Radio Mail Server. An RMS Gateway is an RMS that is connected via the internet to the Common Message Server.
  Can connect to other RMS stations
CMS: Common Message Server. The CMS is the Winlink server that is situated in the ‘internet’.
Radio‐Only Operation: This consists of RMS stations that can auto‐forward by RF, independent of internet availability.
Peer-to-Peer: Direct contact between two client stations.
MID: Message ID. This is a unique alpha‐numeric code (e.g. YFYJDP7P2GFJ) that is assigned to each message.

## Slide 7: Architecture
CMS
RMS
(gateway)
Client
(you)

## Slide 8: Paths
CMS / RMS
  Internet required
Radio-Only Mode
  No internet used
  RMS to RMS
Peer to Peer (P2P)
  Direct user to user
Mesh Networks
  Wireless access points
  Custom ham firmware
Telnet
  Direct to internet – skips radio

## Slide 9: Shack Setup
Radio / Antenna
Audio Interface
  TNC or PC sound card interface
Computer
Winlink software

## Slide 10: Communications Protocols
Telnet
Packet
Pactor
Ardop
VARA
Iridium GO
AX.25 (VHF/UHF)

## Slide 11: How Does It Work?
Just like any email client you use
  But a few extra steps
Attachments
  Size should be limited
  At 300 baud (typical HF rate) or 1200 baud on VHF can take a while
  89kb
    VHF - 1 minute
    HF - 9+ minutes
    f(signal quality)
HTML forms

## Slide 12: Costs
Winlink Express maintained by the Amateur Radio Safety Foundation:
  Free
  $24 to support but not required
  Donate to support
All others: Free
Vara:
  Free – limited data rate
  $69 – Unlimited data rate
  FM / HF / Satellite

## Slide 13: Encryption
Yes per your radio service in your country
MARS and SHARES – yes
US ‘amateur’ radio – no
However, since it’s beeps and squeaks, a bit more sophistication is needed to listen in
  Hence why American Red Cross in MD likes to use it as it affords a bit more privacy

## Slide 14: Winlink Tools – Traffic Activity
Apr 2023 – 92,804 msgs
Dec 2025 – 102,563
Vara most popular (Dec 25)
  HF - ~18,000 connections
  VHF - ~46,000
Avg size: 5,474 Bytes
https://winlink.org/RMSChannels
Traffic tab

## Slide 15: Winlink Account
Download and install Client software
Winlink Express
  Normally when starting for the 1st time
Others follow their instructions
Email account: callsign@winlink.org
https://winlink.org/user

## Slide 16: Winlink Message Viewer
Saved 21 days
Searchable
…assist users with US FCC amateur radio rules compliance
https://winlink.org/content/us_amateur_radio_message_viewer

## Slide 17: Software Options
Programs | Outpost | AirMail | WoAD | Pat | RadioMail | Paclink-Unix | Paclink | Winlink Express
Supported OS, CPU | Any | Win95 & up | Android 4.1 & up | Linux, Mac OSX, Android Win64/32 | iOS | Linux, FreeBSD, x86, x86_64, MIPS, ARM | Windows 8 & up | Windows 8 & up
Recommended uses | Single-user, | Single-user, | Single-user, Routine, EmComm | Single-user, | Single-user | Casual single-user, | Single-user, | Single-user,
 | EmComm on packet networks | Routine, |  | Limited EmComm |  | Limited EmComm | Multi-user, | Multi-user/multi-account,
 |  | Maritime |  |  |  |  | Routine, | Routine,
 |  |  |  |  |  |  | EmComm | Maritime,
 |  |  |  |  |  |  |  | EmComm
Tactical address support | Yes | No | Yes | Yes | Yes | No | Yes | Yes
TELNET | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
AX.25 PACKET | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
ARDOP | No | No | Yes | Yes | No | No | No | Yes
VARA HF and VARA FM | No | No | Yes, limited | Yes, limited | Yes, limited | No | No | Yes.
Peer-to-peer contacts | Yes | Yes | Yes | Yes | Yes, outbound | No | No | Yes
https://winlink.org/ClientSoftware

## Slide 18
WINLINK
RMS Express Forms
Files common to all Forms

## Slide 19: What Winlink Offers for EmComm
Flexibility:
  Internet-only (Telnet) direct connections to Winlink.
  Radio link bridge to Internet e-mail
  Radio-only store and forward messaging
  Peer-to-peer connections between radio end-users
  Various levels of security including message encryption
Interoperability: Connect different types of systems
  Bridge different radio capabilities (VHF/UHF/HF)
  Bridge protocols: Pactor, Winmor, Packet
  Seamless integration with Internet e-mail
Geographical dispersion and redundancy for reliability

## Slide 20: What Winlink Offers for EmComm
Standard e-mail format with many features
  Binary file attachments (pictures, pdf, spreadsheets)
  Automatic message compression/decompression
Time independence (except for peer-to-peer)
Good operation at most power levels
Not limited by station-to-station propagation
Message logging, and ICS report generation
Wide adoption by EmComm related agencies

## Slide 21: WinLink Express

## Slide 22: Download and Install
Winlink Express
  https://downloads.winlink.org/User%20Programs/
VARA HF and VARA VHF – EA5HVK
  https://rosmodem.wordpress.com/
  Look at files on page for ideas / manuals

## Slide 23: Winlink Express Landing Window

## Slide 24: Top Tool Bar

## Slide 25: Settings & Message

## Slide 26: Winlink Express Setup

## Slide 27: Winlink Express Initial Setup
3 Main Windows
  WinLink Express
  Vara HF Winlink Session (click open session)
  Vara
Setting in Winlink Express
  Basic User Info
Setting in Session
  Vara TNC Setup
  Radio Setup
Settings in VARA HF
  VARA Setup
  Sound Card
VARA Session
Winlink Express
VARA HF TNC

## Slide 28: Winlink Express Operations

## Slide 29: Composing Messages
In the main window select Message > New Message
TO: just the call sign or full email address
Subject
Free text in window
Just like a real email
Click post to outbox
Then open session for VARA HF Winlink or preferred session

## Slide 30: ICS-213 General Message
HTML Form in browser

## Slide 32: Send As
Winlink message default
Radio-only – all RF (Winlink message)
Peer-to-Peer only sends if connected to the receiving station and addressed to that receiving station

## Slide 33: Open Session
Select session mode
Click “Open Session:”
Opens connection to radio

## Slide 34: Open Session

## Slide 35: Vara HF Session
Indicates you’ve successfully connected to radio
Channel Selection

## Slide 36: Find RMS (Gateway) To Send Message To
Click ‘Channel Selection’
Will take a while to populate
  I do via internet
Highlight and select
Will populate into VARA HF Winlink Session
  Can save as a favorite
  Will tune radio to right freq when you click ‘start’

## Slide 37
“Start” to connect

## Slide 38
Gap means no data
Note: 8000 bps
this is FM
HF normal for me is about 200bps
S/N in green during RX = good
Progress Bar
L to R = TX
R to L = RX

## Slide 39: Closing Thoughts
Fun to play with
Can impress non-Ham friends with emails
If you use other digital modes – easier to setup
Questions / Thoughts / Need Help Setting Up
  Email: N4RAF@winlink.org

## Slide 40: Backups and Imported

## Slide 41: Settings – Winlink Express
Enter your data
Call sign
Grid Square
Contact info

## Slide 42: Settings – Vara HF Setup Radio Setup
Click settings
  VARA TNC Setup 1st
  Radio Setup 2nd
  Others not needed
In TNC only thing I changed was the modem location
  And 2nd check box – Show VARA TNC screen

## Slide 43: Settings – VARA HF Radio

## Slide 44: Settings – VARA HF TNC
VARA Setup
Sound Card

## Slide 45: WINLINK Nets

## Slide 46: My Favorites
Winlink Wed
  https://winlinkwednesday.net/
  Weekly and simple
East Coast
  Send winlink email to: east-coast and request to join weekly net
  Weekly a bit more advanced and entertaining – explores Winlinks capabilities
EmComm – Training aka Winlink Thurs
  https://emcomm-training.org/Winlink_Thursdays.html
  2026 – Weekly – you get graded – basically can you follow instructions
MDC Digital EmComm Challenge
  Send winlink email to: MDCWINLINK-1 and request to join
  Monthly – 3 tasks – VARA FM, P2P, VarAC email, Fldigi/Flmsg, etc…
  Aug 25 example: https://k3jsj.net/August-Challenge-Instructions/

## Slide 47: Winlink Wed
https://winlinkwednesday.net/

## Slide 48: What is Winlink Wed
Weekly amateur radio digital net where check-ins are via Winlink
Purpose – practice using Winlink
Supports Virginia EmComm activities
HF and VHF/UHF
Formats
  Standard --- N4RAF, Steve, Leesburg, Loudoun, VA (HF P2P)
  Weather report --- above plus ‘rock is wet and swinging’
  ICS-213
Peer-to-Peer

## Slide 49: Peer-to-Peer

## Slide 50: Winlink Wed Results

## Slide 51: Winlink – Maps

## Slide 52: BACKUP

## Slide 53: RMS – VARA Map
VARA displayed
Others selected from menu at top of map
https://winlink.org/RMSChannels

## Slide 54: RMS – Vara Map – Local
HF RMS nodes
'H' markers - Winlink Hybrid Network participants. They offer RF message forwarding if local internet links are not available.

## Slide 55: RMS Express Forms
HTML Form and Template Set
A full form set has three components:
  A template that displays the form and generates the text message to be sent.
  An input form that solicits input from the user.
  A display form that formats and displays the information on the recipient’s computer.
Input from a form is encapsulated in a compact XML file attached to the message.
The actual form HTML is not transmitted.
Input and display forms may be large, but the actual data transmitted is very compact.
Receiving station must have the display form installed.

## Slide 56: Clients
Winlink Express - https://winlink.org/WinlinkExpress
Outpost - https://www.outpostpm.org/index.php
AirMail - http://www.siriuscyber.net/ham/
Pat - https://getpat.io/ (cross platform, written in Go)
WoAD - https://woad.sumusltd.com/ (Android)
Paclink - https://winlink.org/Paclink (gateway to normal e-mail clients)
Winlink FAQs: https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=web&cd=&ved=2ahUKEwi37ee5mYD_AhUfFlkFHRB4D38QFnoECBIQAw&url=https%3A%2F%2Fwinlink.org%2Fsites%2Fdefault%2Ffiles%2Fdownload%2Fwl2k_faq_20230311.pdf&usg=AOvVaw3uO-QgLPwRUD0h5pCQ2uQ-